## Slide 1: LRB Design Review
November 2025

## Slide 2: Research Mission Overview
Student Organization for Aerospace Research

## Slide 3: Purpose
Student Organization for Aerospace Research
Launch Rail Board (LRB)
Replacing the Signal Observations Board (SOB) from Ouroboros
Interface with Anemometers, Thermocouples, and Load Cells by launch rail
Communicates with FSB over simplex UART via RS485 to communicate data

## Slide 4: Physical Board
Student Organization for Aerospace Research
Board is on launch rail
Encased in waterproof housing

## Slide 5: Research Mission FSB Connection
Student Organization for Aerospace Research

## Slide 6: Connection
Student Organization for Aerospace Research
Provide Power: 48V DC
Communicates using simplex UART over RS-485 twisted pair

## Slide 7: Connectors
Student Organization for Aerospace Research
Off board 8 pos keyed Molex
On PCB and cable goes to box edge waterproof connector
Header: 0430450800 https://www.digikey.ca/en/products/detail/molex/0430450800/252529
Cable: 2147561082 https://www.digikey.ca/en/products/detail/molex/2147561082/12180697?s=N4IgTCBcDa4IwBYDsBWAbHADADggXQF8g

## Slide 8: Connectors
Student Organization for Aerospace Research
Off board 8 pos waterproof circular connector
Communicates using simplex UART over RS-485 twisted pair
Box Edge: 54-00184 https://www.digikey.ca/en/products/detail/tensility-international-corp/54-00184/13548494
Cable: M12A08MR-12AMR-SD005 https://www.digikey.ca/en/products/detail/amphenol-ltw/M12A08MR-12AMR-SD005/21315761

## Slide 9: Research Mission Power Regulation
Student Organization for Aerospace Research

## Slide 10: Over View
Student Organization for Aerospace Research
48V in from Fill Systems Board
Buck converter down to 10V
LDO down to 5V
5V LDO or USB power through another LDO down 3V3
48V FSB
LDO 5V
Buck 10V
LDO 3V3
USB 5V

## Slide 11: Buck
Student Organization for Aerospace Research
TPS54561DPRT Buck
Layout from Webench SVG
Vout=10V, Vref=0.8V
Lots of smoothing, bulk capacitance
Rfbt=100k, Rfbb=8.66k, Rfbt/Rfbb=11.547, Rfbt/Rfbb=(Vout-Vref)/Vref=11.5

## Slide 12: LDOs
Student Organization for Aerospace Research
For 5V: R1=15.8k, R2=47.5k
  With these vals: Vout=4.98V
For 3.3V: R1=45.3, R2=75k
  With these vals: Vout=3.298V

## Slide 13: USB Power and ORing
Student Organization for Aerospace Research
ORing Circuit prioritizes power from the FSB over the USB

## Slide 14: Split Power Plane
Student Organization for Aerospace Research
The third layer of the board is a power plane
It has two 5V sections
So like hopefully that isn’t a problem
If it is I probably won’t change it so like…
We can pray together

## Slide 15: Research Mission Sensors
Student Organization for Aerospace Research

## Slide 16: Sensor Overview
Student Organization for Aerospace Research
3x Thermocouples (TC) – Using AFE with SPI output
2x Load Cells (LC) – Using AFE with I2C output
1x Anemometer: Analog output through resistor divider to MCU ADC

## Slide 17: Sensor Connector
Student Organization for Aerospace Research
M12 screw, 5 position circular board to wire connector 54-00247
All sensors use the same connector
Waterproof box edge connector:
  https://www.digikey.ca/en/products/detail/tensility-international-corp/54-00247/13548445
Cable:
  https://www.digikey.ca/en/products/detail/tensility-international-corp/50-00960/13548425

## Slide 18: Thermo Couples
Student Organization for Aerospace Research
Took this from the Sensor Dev Board so if anything is wrong blame Will
Uses SPI. The CS has a pull up in the MCU schematic doc

## Slide 19: Load Cells
Student Organization for Aerospace Research
Took this from the Sensor Dev Board so if anything is wrong blame Will
Uses I2C. The SCL and SDA has a pull up in the MCU schematic doc

## Slide 20: Annemometer Sensor
Student Organization for Aerospace Research
Hold your applause for this one
This one is all me, Will did none of this
Output connects to MCU ADC

## Slide 21: Research Mission Memory
Student Organization for Aerospace Research

## Slide 22: Flash Memory Chip
Student Organization for Aerospace Research
Using W25N04KVZEIR
4Gbit capacity
QuadSPI Interface to QuadSPI1 on STM
16bit * 4sensors + 32bonus bits = 96bit/sample
(96bit/sample)*(1000samples/s)*(1byte/8bits) = 12kB/s`
For 6 hours we need 259.2MB or 2073.6Mbit

## Slide 23: Research Mission USB File System
Student Organization for Aerospace Research

## Slide 24: USB C Interface
Student Organization for Aerospace Research
USB C connection for FS data transfer and low voltage power supply
USB data differential pair with an impedance of 90Ω which causes a trace width of 4.3mils (min trace width is 4mils at JLC PCB)
USB connects to the only USB on the STM32G491ME, pins PA11, PA12

## Slide 25: Research Mission Microcontroller
Student Organization for Aerospace Research

## Slide 26: Overview
Student Organization for Aerospace Research
Using the STM32G491ME
Smaller and cheaper package
Not the H7

## Slide 27: Oscillator
Student Organization for Aerospace Research
Using the ABM8-32.000MHZ-B2-T https://www.digikey.ca/en/products/detail/abracon-llc/ABM8-32-000MHZ-B2-T/2001197
Oscillator has CL=18pF, and CS=6pF
For CL1 and CL2 = 24pF based on CL1​=CL2​=2∗(CL​−CS​)
The STM specifies Gm,crit=1.5mA/V
With CL1/CL2, Gm,crit,osc=2.8524mA/V
RExt=221Ω, see https://www.st.com/resource/en/application_note/an2867-guidelines-for-oscillator-design-on-stm8afals-and-stm32-mcusmpus-stmicroelectronics.pdf

## Slide 28: Power Supply
Student Organization for Aerospace Research
STM takes 1.7V-3.6V, it’s connected to 3V3 line
Lots of Caps

## Slide 29: Connectivity Memory
Student Organization for Aerospace Research
Flash memory uses Quad SPI 1
  PE12:IO0
  PB0:IO1
  PE14:IO2
  PE15:IO3
  PE10:CLK
  PE11:NCS

## Slide 30: Connectivity Thermocouples
Student Organization for Aerospace Research
Thermocouples connect to SPI1 and use 9 GPIOs for TC1, TC2, TC3 respectively:
  CS (SS): PD2, PB6, PD9
  nDRDY: PB4, PB7, PD8
  nFault: PD1, PB5, PD10

## Slide 31: Connectivity Load Cells
Student Organization for Aerospace Research
Load Cells connect to I2C3 and use:
  SDA: PC9
  SCL: PC8
Rp=4.7kΩ

## Slide 32: Connectivity Anemometer
Student Organization for Aerospace Research
Anemometer use ADC1 IN1 on pins:
  PA0: AN+
  PA1: AN-
AN- has 0Ω jumper to ground if sensor only provides single ended.

## Slide 33: Connectivity FSB
Student Organization for Aerospace Research
FSB connects using USART3 in async mode:
  UART Tx: PB10
  UART Rx: PB11
  RS-485 DE: PB14
Can use built in DE hardware flow control for UART to RS-485 chip

## Slide 34: Programming
Student Organization for Aerospace Research
Use 12 pin keyed 2.54mm molex connector for Serial Wire Debug Programming protocol
0702461201:
https://www.digikey.ca/en/products/detail/molex/0702461201/760167
0022552122:
https://www.digikey.ca/en/products/detail/molex/0022552122/313630
0016020074:
https://www.digikey.ca/en/products/detail/molex/0016020074/4838840

## Slide 35: Debug
Student Organization for Aerospace Research
Programming Debug UART uses USART2 (PA2:Tx, PA3:Rx)
Debug LEDs
  On board 3x: PC13, PC14, PC15
  External (box edge) LEDs: PA15, PC10, PC11, PC12, PD0
S2B-XH-A
XHP-2
SXH-001T-P0.6N
https://www.aliexpress.com/item/1005009023296115.html

## Slide 36: Debug Buzzer
Student Organization for Aerospace Research
Debug Buzzer Same Sky CMI-1210-5-95T
  Connects to PWM PC0: TIM1, PWM Gen CH1
  95dB, plug your ears

## Slide 37: Debug Test Points
Student Organization for Aerospace Research
Power Test Points (Stupid Orange Ones):
  10V, 5V-FSB, VBUS-USB, 5V, 3V3
Signal Test Points (1206 Clips):
  I2C lines
  SPI lines (including CS)
  Debug UART
  and FSB UART (with DE)

## Slide 38: Research Mission THE END
Student Organization for Aerospace Research